## Slide 1: ESI measurement conditions
Thermo Scientific ExactivePlus
HESI ion source
R = 70.000
Sheath gas flow rate 15
Aux gas flow rate 10
Sweep gas flow rate 0
Spray voltage 3.30 kV
Capillary temperature 320 °C
S-lens RF level 50.0
Aux gas heater temp 50 °C
Solvent flow rate 20 µL/min
Methanol
Average deviation of experimental and calculated masses approx. 1 mDa
Calibration date: 05.01.2022

## Slide 2: MB9v1

## Slide 3: MB9v1
[M+H]+
D(m/z) = -0.9 mDa
[M+Na]+
D(m/z) = -0.9 mDa
[M+K]+
D(m/z) = -0.9 mDa

## Slide 4: MB9v1
[2M+H]+
D(m/z) = -1.4 mDa
[2M+Na]+
D(m/z) = -1.8 mDa

## Slide 5: MB10v1
assignments similar to MB9v1
m/z = 339 Da → [M-CH4] ???

## Slide 6: MB10v1
assignments similar to MB9v1
m/z = 339 Da ???
integer difference 355-339 = 16
but simulation does not match CH4, O, NH2 …

## Slide 7: MB15v2
assignments similar to MB9v1

## Slide 8: MB19v1
assignments similar to MB9v1

## Slide 9: MB20c44

## Slide 10: MB20c44
[M+H]+
D(m/z) = -0.8 mDa
[M+Na]+
D(m/z) = -1.0 mDa
[M+K]+
D(m/z) = -1.0 mDa

## Slide 11: MB20c44
[2M+Na]+
D(m/z) = -2.1 mDa
[2M+Na]+
D(m/z) = -2.3 mDa

## Slide 12: MB25v3

## Slide 13: MB25v3
[M+H]+
D(m/z) = -0.4 mDa
[M+Na]+
D(m/z) = -0.8 mDa

## Slide 14: MB25v3
[2M+Na]+
D(m/z) = -1.2 mDa

## Slide 15: MB26v1
assignments similar to MB25v3

## Slide 16: MB82v5

## Slide 17: MB82v5
[M+H]+
D(m/z) = -0.2 mDa
[M+Na]+
D(m/z) = -0.2 mDa
?
?
?

## Slide 18: MB118

## Slide 19: MB118
[M+H]+
D(m/z) = -0.7 mDa
[M+Na]+
D(m/z) = -0.7 mDa
[M+K]+
D(m/z) = -0.6 mDa

## Slide 20: MB118
[2M+H]+
D(m/z) = -1.4 mDa
[2M+Na]+
D(m/z) = -1.8 mDa

## Slide 21: MB145v1

## Slide 22: MB145v1
[M+H]+
D(m/z) = -0.5 mDa